## Slide 1: Master Thesis Initial Report - Research on Modulation and Control Optimization for MMC-SST
Presenter: Haoheng Li
Supervisor: Dr. Gean Maia de Sousa
Professor: Prof. Dr.sc. ETH Zürich Marcelo Lobo Heldwein
Technical University of Munich
12, December, 2025

## Slide 2: Outline
Introduction
Problem Statement and Research Gap
Objective & Methodology
Notes: Let's begin with the outline. I'll start with an introduction, followed by detailed explanations of Observer-Based Methods and Switching-State-Based Methods, including a simulation study. Finally, I'll provide a comparison of these methods, discuss future research directions, and conclude with a summary.

## Slide 3: What is SST and its application
State-of-art middle voltage interface for AC-DC
Solid state transformer middle voltage interface
A Solid State Transformer (SST) is a power electronic converter with Middle-Frequency Transformer (MFT).
Key Advantages:
Volume/Weight reduction (due to high frequency).
Full power flow control (Active/Reactive).
Higher efficiency for AC-DC application

## Slide 4: What is SST and its application
Comparison of SST and Low Frequency Transformer(LFT) Solution
AC-AC
50% AC-AC and 50% AC-DC
AC-DC
Data Center
Super Charge station

## Slide 5: Outline
Introduction
Problem Statement and Research Gap
Objective & Methodology
Notes: Let's begin with the outline. I'll start with an introduction, followed by detailed explanations of Observer-Based Methods and Switching-State-Based Methods, including a simulation study. Finally, I'll provide a comparison of these methods, discuss future research directions, and conclude with a summary.

## Slide 6: Topology Analysis -Mudular Multilevel Converter (MMC)-SST
10kV 50Hz Middle Voltage AC
Middle Frequency square wave
800V DC Voltage

## Slide 7: Existed Modulation Method
Nearest Level Modulation
✅ Very Low Losses
❌ Poor Waveform Quality (High THD)
DC/DC Stage Challenge
MMC AC-AC Stage
Phase Shift modulation
❌ Limited Phase Shift control for the MFT to ensure Zero Voltage Switching (ZVS).
Pulse Width Modulation
✅ Good Harmonic performance
❌ Huge Switching Losses

## Slide 8: Outline
Introduction
Problem Statement and Research Gap
Objective & Methodology
Notes: Let's begin with the outline. I'll start with an introduction, followed by detailed explanations of Observer-Based Methods and Switching-State-Based Methods, including a simulation study. Finally, I'll provide a comparison of these methods, discuss future research directions, and conclude with a summary.

## Slide 9: Objectives
Core objective: Develop a Optimized Modulation and Control Scheme for MMC-SST
Specific Goals (Key Performance Indicators):
Minimize in SMs: Reduce switching losses in the MMC arms.
Maximize MFT Efficiency: Ensure high-frequency operation in the isolation stage.
Capacitor Voltage Balancing: Maintain stable DC voltages across all sub-modules without excessive sorting actions.
Wide range ZVS for DC-DC stage: Develop modulation scheme that has a wider range for ZVS than PSPWM.

## Slide 10: Methodology
Mathematical modeling
AC-AC MMC
DAB
Analysis of existed modulation and control methods for MMC-SST
Research on modulation and control optimization
Hybrid modulation scheme for MMC AC-AC stage
Pulse amplitude control (PAC) for the DAB DC-DC stage for wide range ZVC
C code to implementing voltage balancing for submodules.
Simulation verification using PLECS
Verifying the method using PLECS
Compared the proposed method with the existing

## Slide 11: Expected Outcome
Theoretical Model: Mathematical derivation of the modulation strategy.
Simulation Model: A complete, running MMC-SST model in PLECS.
Performance Comparison (The Evidence):
  Efficiency
  THD Analysis
  Switching Count Reduction
Contribution: A novel balancing algorithm that decouples sampling frequency from switching frequency.

## Slide 12: Timeline
2025
2026
Nov
Dec
Jan
Feb
Mar
Apr
May
Thesis writing
DAB PS
Research
MMC AC-AC
Proposing method
DAB PAC
PAC DAB
Modeling
modulation
MMC DC-AC
Literature research
Simulation
Final report
Midterm report
Introduction
Initial report
MMC AC-AC
Existing research
MMC-SST
Math model
Proposed method
Thesis submission
Simulation result
Status
Proposed method
Activity
Comparision
MMC DC-AC

## Slide 13: Thank You & Questions
Presenter: Haoheng Li
Supervisor: Dr. Gean Maia de Sousa
Technical University of Munich
12, Dec, 2025
Notes: That concludes my presentation. Thank you very much for your attention. I’d be happy to take any questions.加